Casio fx502p fx602p Interface

The Expansion Port

### Pin functions
Expansion Port Pin	Symbol	Function
1	CE	Chip enable output, active high
2	GND	Ground (positive supply voltage rail)
3	D8	Data input/output (bi-directional)
4	CONT	-3V when operational, 0V when stand-by
5	OP	Selects the Command Register (OP=0) or Data Register (OP=1)
6	VDD1	-3V (negative supply voltage rail)
7	SP	Clock output

Additional commands used by the FX-602P
Code	Function	Description
001100	Wait	This command suspends the data transfer for a while when reading from the tape. The calculator issues it after loading of the file header, then reads a single data bit. The meaning of this value is unknown to me (the interface always returns 1).
110100	Counter	This command defines the frequency of the music tone. It expects an 8-bit value (the least significant bit first).
frequency = 32768Hz/value
001110	Play the sound	After sending this command, signal of frequency specified by the Counter command appears on the MIC output.
111110	Stop the sound	This command terminates generating the music tone.
111100	Close	Apart from closing the communication channel, this command has an additional function.After sending it, the calculator can read a single data bit which returns the Cal/Music switch state (Cal=0, Music=1). Otherwise, this switch doesn't seem to influence the function of the controller.
Example of playing music
1. OP=0 111100 ;test the Cal/Music switch
    OP=1 1 ;returned value=1,
        ;means the switch in the "Music" position
2. OP=0 111110	;stop the sound
3. OP=0 110100 ;preset the counter according to the note pitch
    OP=1 01001010 ;value=0x52 (frequency=400Hz)
4. OP=0 001110 ;play the sound
5. delay depending on the tempo
6. goto 1, until all notes played
7. OP=0 000000 ;reset
8. OP=0 111110	;stop the sound

fx602p power on sequence (gadget)

+++Buffer Count:11
*0 19 (6 bits)
*1 03 (6 bits)
*2 00 (1 bits)
*3 1B (6 bits)
*4 03 (6 bits)
*5 00 (1 bits)
*6 19 (6 bits)
*7 03 (6 bits)
*8 00 (1 bits)
*9 00 (6 bits)
*10 3E (6 bits)

fx602p inv save EXE sequence:

*11 19 (6 bits)
*12 07 (6 bits)
*13 07 (6 bits)
*14 0E (7 bits)
*15 28 (6 bits)
*16 04 (6 bits)
*17 00 (1 bits)
*18 04 (6 bits)
*19 00 (1 bits)
*20 04 (6 bits)
*21 00 (1 bits)
*22 04 (6 bits)
*23 00 (1 bits)
*24 04 (6 bits)
*25 00 (1 bits)
*26 04 (6 bits)
*27 00 (1 bits)
*28 04 (6 bits)
*29 00 (1 bits)
*30 04 (6 bits)
*31 00 (1 bits)
*32 04 (6 bits)
*33 00 (1 bits)
*34 04 (6 bits)
*35 00 (1 bits)
*36 04 (6 bits)
*37 00 (1 bits)
*38 04 (6 bits)
*39 00 (1 bits)
*40 04 (6 bits)
*41 00 (1 bits)
*42 04 (6 bits)
*43 00 (1 bits)
*44 04 (6 bits)
*45 00 (1 bits)
*46 04 (6 bits)
*47 00 (1 bits)
*48 00 (6 bits)
*49 00 (1 bits)
*50 04 (6 bits)
*51 00 (1 bits)
*52 04 (6 bits)
*53 00 (1 bits)
*54 04 (6 bits)
*55 00 (1 bits)
*56 04 (6 bits)
*57 00 (1 bits)
*58 04 (6 bits)
*59 00 (1 bits)
*60 0C (6 bits)
*61 00 (1 bits)
*62 04 (6 bits)
*63 00 (1 bits)
*64 04 (6 bits)
*65 00 (1 bits)
*66 04 (6 bits)
*67 00 (1 bits)
*68 0C (6 bits)
*69 00 (1 bits)
*70 04 (6 bits)
*71 00 (1 bits)
*72 04 (6 bits)
*73 00 (1 bits)
*74 04 (6 bits)
*75 00 (1 bits)
*76 0C (6 bits)
*77 00 (1 bits)
*78 04 (6 bits)
*79 00 (1 bits)
*80 04 (6 bits)
*81 00 (1 bits)
*82 04 (6 bits)
*83 00 (1 bits)
*84 0C (6 bits)
*85 00 (1 bits)
*86 04 (6 bits)
*87 00 (1 bits)
*88 04 (6 bits)
*89 00 (1 bits)
*90 04 (6 bits)
*91 00 (1 bits)
*92 0C (6 bits)
*93 00 (1 bits)
*94 04 (6 bits)
*95 00 (1 bits)
*96 04 (6 bits)
*97 00 (1 bits)
*98 04 (6 bits)
*99 00 (1 bits)
*100 0C (6 bits)
*101 00 (1 bits)
*102 04 (6 bits)
*103 00 (1 bits)
*104 04 (6 bits)
*105 00 (1 bits)
*106 04 (6 bits)
*107 00 (1 bits)
*108 0C (6 bits)
*109 00 (1 bits)
*110 04 (6 bits)