Casio fx502p fx602p Interface

The Expansion Port

### Pin functions
Expansion Port Pin	Symbol	Function
1	CE	Chip enable output, active high
2	GND	Ground (positive supply voltage rail)
3	D8	Data input/output (bi-directional)
4	CONT	-3V when operational, 0V when stand-by
5	OP	Selects the Command Register (OP=0) or Data Register (OP=1)
6	VDD1	-3V (negative supply voltage rail)
7	SP	Clock output

Additional commands used by the FX-602P
Code	Function	Description
001100	Wait	This command suspends the data transfer for a while when reading from the tape. The calculator issues it after loading of the file header, then reads a single data bit. The meaning of this value is unknown to me (the interface always returns 1).
110100	Counter	This command defines the frequency of the music tone. It expects an 8-bit value (the least significant bit first).
frequency = 32768Hz/value
001110	Play the sound	After sending this command, signal of frequency specified by the Counter command appears on the MIC output.
111110	Stop the sound	This command terminates generating the music tone.
111100	Close	Apart from closing the communication channel, this command has an additional function.After sending it, the calculator can read a single data bit which returns the Cal/Music switch state (Cal=0, Music=1). Otherwise, this switch doesn't seem to influence the function of the controller.
Example of playing music
1. OP=0 111100 ;test the Cal/Music switch
    OP=1 1 ;returned value=1,
        ;means the switch in the "Music" position
2. OP=0 111110	;stop the sound
3. OP=0 110100 ;preset the counter according to the note pitch
    OP=1 01001010 ;value=0x52 (frequency=400Hz)
4. OP=0 001110 ;play the sound
5. delay depending on the tempo
6. goto 1, until all notes played
7. OP=0 000000 ;reset
8. OP=0 111110	;stop the sound

fx602p power on sequence (gadget)

+++Buffer Count:11
*0 19 (6 bits)
*1 03 (6 bits)
*2 00 (1 bits)
*3 1B (6 bits)
*4 03 (6 bits)
*5 00 (1 bits)
*6 19 (6 bits)
*7 03 (6 bits)
*8 00 (1 bits)
*9 00 (6 bits)
*10 3E (6 bits)

fx602p inv save EXE sequence:

*11 19 (6 bits)
*12 07 (6 bits)
*13 07 (6 bits)
*14 0E (7 bits)
*15 28 (6 bits)
*16 04 (6 bits)
*17 00 (1 bits)
*18 04 (6 bits)
*19 00 (1 bits)
*20 04 (6 bits)
*21 00 (1 bits)
*22 04 (6 bits)
*23 00 (1 bits)
*24 04 (6 bits)
*25 00 (1 bits)
*26 04 (6 bits)
*27 00 (1 bits)
*28 04 (6 bits)
*29 00 (1 bits)
*30 04 (6 bits)
*31 00 (1 bits)
*32 04 (6 bits)
*33 00 (1 bits)
*34 04 (6 bits)
*35 00 (1 bits)
*36 04 (6 bits)
*37 00 (1 bits)
*38 04 (6 bits)
*39 00 (1 bits)
*40 04 (6 bits)
*41 00 (1 bits)
*42 04 (6 bits)
*43 00 (1 bits)
*44 04 (6 bits)
*45 00 (1 bits)
*46 04 (6 bits)
*47 00 (1 bits)
*48 00 (6 bits)
*49 00 (1 bits)
*50 04 (6 bits)
*51 00 (1 bits)
*52 04 (6 bits)
*53 00 (1 bits)
*54 04 (6 bits)
*55 00 (1 bits)
*56 04 (6 bits)
*57 00 (1 bits)
*58 04 (6 bits)
*59 00 (1 bits)
*60 0C (6 bits)
*61 00 (1 bits)
*62 04 (6 bits)
*63 00 (1 bits)
*64 04 (6 bits)
*65 00 (1 bits)
*66 04 (6 bits)
*67 00 (1 bits)
*68 0C (6 bits)
*69 00 (1 bits)
*70 04 (6 bits)
*71 00 (1 bits)
*72 04 (6 bits)
*73 00 (1 bits)
*74 04 (6 bits)
*75 00 (1 bits)
*76 0C (6 bits)
*77 00 (1 bits)
*78 04 (6 bits)
*79 00 (1 bits)
*80 04 (6 bits)
*81 00 (1 bits)
*82 04 (6 bits)
*83 00 (1 bits)
*84 0C (6 bits)
*85 00 (1 bits)
*86 04 (6 bits)
*87 00 (1 bits)
*88 04 (6 bits)
*89 00 (1 bits)
*90 04 (6 bits)
*91 00 (1 bits)
*92 0C (6 bits)
*93 00 (1 bits)
*94 04 (6 bits)
*95 00 (1 bits)
*96 04 (6 bits)
*97 00 (1 bits)
*98 04 (6 bits)
*99 00 (1 bits)
*100 0C (6 bits)
*101 00 (1 bits)
*102 04 (6 bits)
*103 00 (1 bits)
*104 04 (6 bits)
*105 00 (1 bits)
*106 04 (6 bits)
*107 00 (1 bits)
*108 0C (6 bits)
*109 00 (1 bits)
*110 04 (6 bits)

fx502p Gadget Traces

Power On:

First column is packet number
*6358 00 (6 bits) ;
*6359 3E (6 bits) ; Stop command

inv SAVE EXE:

*6364 0C (6 bits)
*6365 00 (1 bits)
*6366 28 (6 bits)
*6367 08 (7 bits)
*6368 08 (7 bits)
*6369 08 (7 bits)
*6370 08 (7 bits)
*6371 08 (7 bits)

08 repeats indefinitely.

FX-502P Opcodes

Modifying a program to try out different invalid codes:

0x3B Displays as F5. xD
0x2B E on load
0x2C Seems to behave like HLT
0x2D E on load
0x2E E on load
0x2F Seems to behave like HLT

0x6A E on load
0x9B inv hyp
0xEA FF-F5-CC (inv hyp ABS) inv hyp sin function
0xEB E on load
0xEC FF-F5-C1 (inv hyp FRAC) inv hyp sin function
0xF5 E on load
0xFB FF-PP NOP
0xFC E on load
0xFD Displays as E3 (+) in mode 2 listing, but when executes shows the step in mode 2 format on LCD then locks up the calculator. Power off is only way to recover.
0xFE Displays as 0C Not sure what it does.
0xFF E on load

You can have multiple programs with the same Pn number. Only the last one seems to be loaded. Also can have different invalid Pn numbers and load doesn’t fail, but code isn’t there.
You can easily renumber programs by altering Pn numbers

Altering the first two bytes of a saved program or data file:

23 01 F0123
23 10 F1023 while loading but won’t load
23 20 F2023
23 30 F3123
23 40 F4023
23 50 E on load
23 60 E on load
23 70 F7023
23 80 F8023
23 90 E on load
23 A0 E on load
23 B0 FP023 (program file)
23 C0 E on load
23 D0 FE023
23 F0 FP023 (Memory load)